## Slide 1
Department of Elecctrical & Electronic Engineering
Khulna University of Engineering & Technology
Bridging Signal and Intelligence: A DSP-Driven EEG Feature Pipeline for Neural Network Seizure Detection
Presented By
Md. Ohiduzzaman Sajol (2003043)
Durjoy Sarkar Dhrubo (2003026)
EE 4142 – Sessional on Digital Signal Processing
Presented On
November 2, 2025
Presented To
Dr. Monira Islam
Associate Professor, Dept. of EEE, KUET

## Slide 2
Outline
Abstract
Introduction
Background
Methodology
Results
Discussion
Conclusion
Future Work
References
EE 4142 – Sessional on Digital Signal Processing

## Slide 3
Abstract
DSP-based EEG pipeline for seizure detection
CHB-MIT dataset with notch & bandpass filters
Extracted spectral & statistical EEG features
Visualized raw vs. filtered & frequency spectra
Features ready for ML seizure classification
EE 4142 – Sessional on Digital Signal Processing

## Slide 4
Introduction
EEG is a non-invasive method to measure brain activity.
Automated EEG-based seizure detection is a key biomedical DSP task.
EEG’s non-stationary nature demands strong preprocessing & feature extraction.
DSP provides tools for time–frequency domain analysis (e.g., convolution, DFT, filtering).
EEG data (CHB-MIT) is preprocessed, features extracted, and prepared for ML seizure classification.
EE 4142 – Sessional on Digital Signal Processing

## Slide 5
Background: EEG and Seizure Activity
EEG records brain’s electrical signals via scalp electrodes.
Typical EEG range: 0.5–70 Hz, divided into standard bands:
  Δ (0.5–4 Hz) – Deep sleep
  θ (4–8 Hz) – Drowsiness/meditation
  α (8–13 Hz) – Relaxed wakefulness
  β (13–30 Hz) – Active focus
  γ (30–70 Hz) – Cognitive processing
Seizures: sudden, synchronized bursts of activity
  visible as amplitude spikes & spectral power changes
EE 4142 – Sessional on Digital Signal Processing

## Slide 6
Methodology: Data Acquisition
Dataset: CHB-MIT Scalp EEG Database (pediatric epilepsy patients)
Format: EDF files with multi-channel EEG recordings
Loaded via mne.io.read_raw_edf()
Includes both seizure and non-seizure intervals
EE 4142 – Sessional on Digital Signal Processing

## Slide 7
Methodology: Preprocessing Pipeline
Notch Filter (60 Hz): remove power-line noise (IIR notch)
Bandpass FIR Filter (0.5–70 Hz): isolate standard EEG range
Segmentation: 10-s overlapping epochs for temporal analysis
Normalization: z-score (zero mean, unit variance) for consistency
EE 4142 – Sessional on Digital Signal Processing

## Slide 8
Methodology: DSP Operations
Correlation: inter-channel Pearson correlation matrices
Convolution: moving-average smoothing to reduce fluctuations
Spectral Analysis: FFT + Welch PSD for frequency and band-power estimation
EE 4142 – Sessional on Digital Signal Processing

## Slide 9
Methodology: Feature Extraction
Band Powers: mean, std, median in δ, θ, α, β, γ bands
Statistical: energy, variance, skewness, kurtosis
Spectral Entropy: Shannon entropy of normalized PSD
Correlation Metrics: mean, std, max of inter-channel correlations
Band Ratios: e.g., α / β for cognitive state insight
EE 4142 – Sessional on Digital Signal Processing

## Slide 10
Methodology: Implementation
Tools: Python 3.10, MNE, SciPy, NumPy, pandas, Matplotlib
Interactive workflow via Jupyter Notebook
Features aggregated into chb_features.csv
Repository: github.com/projectohid/4142-project
EE 4142 – Sessional on Digital Signal Processing

## Slide 11
Results: Spectrogram Analysis (Normal vs. Seizure)
Normal EEG (Fig. 1) : Broad spectral power (10–30 Hz, α & β bands)
Seizure EEG (Fig. 2) : Dominant low-frequency power (<10 Hz, δ & θ)
Confirms effective filtering and distinct physiological vs. pathological patterns
EE 4142 – Sessional on Digital Signal Processing

## Slide 12
Results: Spectrogram Analysis (Normal vs. Seizure)
EE 4142 – Sessional on Digital Signal Processing
Fig. 1: Spectrogram for Chb01_01.edf (non-seizure).

## Slide 13
Results: Spectrogram Analysis (Normal vs. Seizure)
EE 4142 – Sessional on Digital Signal Processing
Fig. 2: Spectrogram for Chb01_03.edf (seizure).

## Slide 14
Results: Raw Vs. Filtered Signal
Time-domain (Fig. 3): Filtered signal smoother; reduced drift & 60 Hz noise
Frequency-domain (Fig. 3): 60 Hz peak suppressed; spectrum confined to 0.5–70 Hz
Verifies notch + FIR bandpass filters effectiveness
EE 4142 – Sessional on Digital Signal Processing

## Slide 15
Results: Raw Vs. Filtered Signal
EE 4142 – Sessional on Digital Signal Processing
Fig. 3: Raw and filtered Signals and their Spectrums for Chb01_01.edf .

## Slide 16
Results: EEG Band Power Distribution
Power hierarchy:
Δ > θ > β > γ > α
Low-frequency dominance → seizure or drowsy state indicator
Confirms spectral accuracy of feature extraction
EE 4142 – Sessional on Digital Signal Processing
Fig. 4: Average Band Power Across EEG Frequency Bands for Chb01_01.edf .

## Slide 17
Results: Time-Domain Statistical Features
High kurtosis: sharp, transient seizure spikes
Low skewness: symmetric yet with frequent outliers
Confirms impulsive, non-Gaussian EEG patterns in seizures
EE 4142 – Sessional on Digital Signal Processing
Fig. 5: Distribution of Statistical Time-Domain Features for Chb01_01.edf .

## Slide 18
Results: Spectral Entropy vs. Delta Power
Negative correlation → higher δ power = lower entropy
Indicates reduced complexity during seizure activity
Validates entropy as nonlinear brain state marker
EE 4142 – Sessional on Digital Signal Processing
Fig. 6: Spectral Entropy vs. Delta Band Power for Chb01_01.edf .

## Slide 19
Results: Inter-Channel Correlation
Max correlation ≈ 1.0: strong cross-channel synchronization
Consistent mean correlation = stable phase coupling
Demonstrates spatial coherence in seizure EEG
EE 4142 – Sessional on Digital Signal Processing
Fig. 7: Distribution of Inter-Channel Correlation Metrics for Chb01_01.edf .

## Slide 20
Results: Feature Matrix & ML Readiness
Each 10 s epoch → 30+ DSP-based features
Seizure/non-seizure epochs clearly separable in feature space
Confirms pipeline suitability for neural network models
EE 4142 – Sessional on Digital Signal Processing
Table I: Part of the extracted Feature Matrix for Chb01_01.edf .

## Slide 21
Results: Summary
EE 4142 – Sessional on Digital Signal Processing
Domain | Key Observation | DSP Technique
Spectrograms | Low-frequency dominance | STFT / Spectrogram
Filtering | Removed 60 Hz & artifacts | Notch + FIR
Band Power | High δ, θ; low α, β, γ | FFT + PSD
Statistics | High kurtosis, low skewness | Time-domain
Entropy | −ve correlation with δ power | Entropy calc.
Correlation | Strong inter-channel sync | Pearson corr.
Feature Set | Clear seizure separation | DSP feature extraction

## Slide 22
Discussion
EE 4142 – Sessional on Digital Signal Processing
Spectral Behavior
  Normal EEG: broad power (10–30 Hz, α–β bands)
  Seizure EEG: strong low-freq. dominance (<10 Hz, δ–θ)
  Confirms shift from desynchronized → synchronized neuronal activity
  Filtering (notch + bandpass) effectively removed 60 Hz noise & drift while preserving core EEG content
Band Power Trends
  Hierarchy: Δ > θ > β > γ > α
  High α/β ratio & reduced high-freq. power → decreased cortical processing during seizures

## Slide 23
Discussion
EE 4142 – Sessional on Digital Signal Processing
Time-Domain Statistics
  High kurtosis: sharp epileptic transients
  Low skewness: symmetric but heavy-tailed amplitude distribution
  Indicates impulsive, non-Gaussian seizure morphology
Entropy & Complexity
  Entropy ↓ as Δ-power ↑ → reduced signal complexity during seizures
  Captures transition to predictable, synchronized brain dynamics
  Entropy = nonlinear complement to power-based metrics

## Slide 24
Discussion
EE 4142 – Sessional on Digital Signal Processing
Inter-Channel Correlation
  High cross-channel correlation (≈1.0) → strong spatial coherence
  Reflects widespread cortical synchronization in seizure states
Integrated DSP Takeways
  Filtering: ensures clean, physiologically valid signals
  FFT / PSD: reveal spectral composition
  Statistics + Entropy: quantify morphology & complexity
  Correlation: captures spatial coupling → Together, classical DSP techniques uncover physiological + pathological EEG patterns, producing interpretable features for intelligent seizure detection.

## Slide 25
Conclusion
EE 4142 – Sessional on Digital Signal Processing
DSP methods effectively applied for EEG seizure analysis.
Filtering + spectral + statistical tools made EEG interpretable.
Key Points:
  Preprocessing: Notch & FIR filters removed noise, kept key signals.
  Spectral: Clear normal–seizure separation (low-freq dominance).
  Stats: High kurtosis, low entropy → synchronized seizure waves.
  Correlation: Strong inter-channel coupling during seizures.
  Features: Compact, ML-ready dataset for classification.
Takeaway: → DSP bridges theory & application, enabling explainable EEG systems.

## Slide 26
Future Work
EE 4142 – Sessional on Digital Signal Processing
Wavelet Filters: Handle dynamic, non-stationary EEG noise.
ICA Cleaning: Remove eye/muscle artifacts.
Deep Learning: Train models on DSP-derived features.
Automation: Streamline preprocessing & feature selection.

## Slide 27
References
EE 4142 – Sessional on Digital Signal Processing
[1] L. Tan and J. Jiang, Digital Signal Processing: Fundamentals and Applications, 3rd ed. Elsevier Science, 2018.
[2] M. Teplan, “Fundamentals of EEG measurement,” Measurement Science Review, vol. 2, no. 2, pp. 1–11, 2002.
[3] H. Adeli, Z. Zhou, and N. Dadmehr, “Analysis of EEG records in an epileptic patient using wavelet transform,” Journal of Neuroscience Methods, vol. 123, no. 1, pp. 69–87, 2003.
[4] U. R. Acharya, S. V. Sree, G. Swapna, R. J. Martis, and J. S. Suri, “Automated EEG analysis of epilepsy: A review,” Knowledge-Based Systems, vol. 45, pp. 147–165, 2013.
[5] A. Aarabi, R. Fazel-Rezai, and Y. Aghakhani, “EEG seizure prediction: Measures and challenges,” Computers in Biology and Medicine, vol. 42, no. 4, pp. 376–390, 2012.

## Slide 28
Department of Elecctrical & Electronic Engineering
Khulna University of Engineering & Technology
Thank You
Any Questions?
EE 4142 – Sessional on Digital Signal Processing